CONTENTS

Product Features and Specifications ............................................1

Installation Requirement ...........................................................3

Steps of Installation…………………………………………………………………………….4

Exploded View ........................................................................31

Test Run.................................................................................35

Operation Instruction ..............................................................37

Maintenance ..........................................................................37

Trouble Shooting ....................................................................38

Parts List ...............................................................................39

I. PRODUCT FEATURES AND SPECIFICATIONS

CLEAR-FLOOR DIRECT-DRIVED MODEL FEATURES

Model A240C  A240CH (See Fig. 1)

· Direct-drived design, minimize the lift wear parts and breakdown ratio

· Dual hydraulic cylinders, designed and made on ANSI standards, utilizing NOK oil seal in cylinder

· Self- lubricating UHMW Polyethylene sliders and bronze bush

· Single-point safety release, and dual safety design

. Clear-floor design, provide unobstructed floor use

. Overhead safety shut-off device prevents vehicle damage

· Supersymmetric arms design, combined adapter

· Standard adjustable heights accommodates varying ceiling heights

| Model | Style | Lifting Capacity | Lifting Time | Lifting Height | Overall Height | Overall Width | Width Between Columns | Minimum Pad Height | Motor |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| A240C | Clear-floor Direct-drived | 4.0T 9,000 lbs | 52S | 1825-1960mm 71 7/8” –77 1/4” | 3621/3821mm 142 1/2”/ 150 1/2” | 3428mm 135” | 2850mm 112 1/4” | 100mm 4” | 2.0/3.0 HP |
| A240CH | Clear-floor Direct-drived | 4.0T 9,000 lbs | 52S | 1825-1960mm 71 7/8” –77 1/4” | 4231/4431 mm 166 1/2” /174 1/2” | 3428mm 135” | 2850mm 112 1/4” | 100mm 4” | 2.0/3.0 HP |

SPECIFICATIONS

Arm Swings View

For Model A240C  A240CH

II. INSTALLATION REQUIREMENT

- TOOLS REQUIRED

  - Rotary Hammer Drill (Φ19)

  - Hammer

  - Level Bar

  - English Spanner (12")

  - Ratchet Spanner With Socket (28#)

(   Wrench set

  - Carpenter’s Chalk

  - Screw Sets

  - Tape Measure (7.5m)

  - Pliers

  - Socket Head Wrench (3#, 5#, 8#)

(  Lock Wrench

(8#, 10#, 13#, 14#, 17#, 19#, 24#)

Fig. 3

B. SPECIFICATIONS OF CONCRETE (See Fig. 4)

Specifications of concrete must be adhered to the specification as following.

Failure to do so may result in lift and/or vehicle falling.

1. Concrete must be thickness 100mm minimum and without reinforcing steel bars, and must be dried totally before the installation.

2. Concrete must be in good condition and must be of test strength 3,000psi minimum.

3. Floors must be level and no cracks.

C. POWER SUPPLY

The electrical source must be 2.2Kw minimum. The source cable size must be 2.5mm² and in good condition of contacting with floor.

III. STEPS OF INSTALLATION

A. Location of Installation

Check and insure the installation location (concrete, layout, space size etc.) is        suitable for lift installation.

B. Use a carpenter’s chalk line to establish installation layout of baseplate (See Fig.5).

C. Check the parts before assembly.

1. Packaged lift and hydraulic power unit (See Fig. 6).

2. Move aside the lift with fork lift or hoist, and open the outer packing carefully

(See Fig.7).

3. Take off the lifting arms and parts box from upper and inside the column, then move them to location nearby installation site (See Fig. 8).

4. Loose the bolts of the upper package stand, take off the upper outer column, take out the parts in the inner column and remove the package stand

5. Move aside the parts and check the parts according to the shipment parts list, and list of parts box. (See Fig. 9, Fig. 10)

Parts box(107)

7. Check the parts of the parts bag 1& 2 according to parts bag list (See Fig. 11 & Fig. 12).

Parts bag 1

Parts bag 2

D. Install parts of extension columns (See Fig. 13).

E. Position powerside column

Lay down two columns on the installation site parallelly, position the powerside column according to the actual installation site. Usually, it is suggested to install powerside column on the front-right side from which vehicles are driven to the lift. This lift is designed with 2-Section columns. Adjustable height according to the ceiling height and connecting the inner and outer columns.

1. When the ceiling height is less than 3850mm (151 1/2”), connecting the outer columns with the upper hole (See Fig.14).

2. When the ceiling height is over 3850mm (151 1/2”), connecting the outer columns

with the lower hole (See Fig.15).

F. Position columns (See Fig. 16)

Position the columns on the installation layout of baseplate, Install the anchor bolts. Check the columns plumbness with level bar, and adjusting with the shims if the columns are not vertical. Do not tighten the Anchor Bolts.

G. Install overhead top beam

1. With help of the hook of top beam, put one side of top beam on top of the extension column and connecting the top beam to extension column by bolts, tighten the bolts. Then assemble the connecting bracket (See Fig. 17).

2. Assemble overhead top beam, tighten the columns anchor bolts (See Fig. 18).

H. Installing the limit switch control bar and limit switch (See Fig.19).

I. Install safety device (See Fig. 20 & Fig. 21).

J. Lift the carriages up to about one meter high by hand and make them be locked at the same level (See Fig.22).

K. Install cables

1. Low setting cable connection. Suitable for ceiling height less than                                                            3850mm (151 1/2”) (See Fig. 23).

2．High setting cable connection. Suitable for the ceiling height over 3850mm (151 1/2”) .

2.1. Cable pass through from the bottom of the carriages and be pulled out from the

open of carriages, then screw the two cable nuts (See Fig. 24).

2.2 Connecting cable for high setting (See Fig. 25).

L．Install safety cable (See Fig. 26)

M. Install motor bracket, hydraulic power unit and oil hose assy.(See Fig. 27)

Tighten all the hydraulic fittings, and fill the reservoir with hydraulic oil.

Note: In consideration of Power Unit’s durability and keep the equipment running in the perfect condition, please use Hydraulic Oil 46#

N. Install control box.(See Fig. 28)

O. Install electrical system

1. Connecting wire with control box (See Fig. 29)

Note: 1) Specification of wire of limit switch and hydraulic solenoid valve is 2×12

2) Wire cable for power source and motor are 4×2.52

3) Using white bobbin to wind around wire

2. Adjusting the current rating of thermal relay in control box according to the different configurations of hydraulic power unit. In general, the electric current of thermal relay should equal or larger than that of motor. The following table shows rated current regulation of thermal relay in case of different hydraulic power unit.

| Hydraulic power unit | PEAK | SPX |
| --- | --- | --- |
|  | 220V 3HP | 380V 3HP | 415V 3HP | 220V 3HP | 380V 3HP |
| Rated current of thermal relay | 16A | 12A | 12A | 18A | 12A |

3. 380V Wire connection and circuit diagram

3.1 Wire connection diagram in the control box (See Fig. 31)

3.2  380V Wire connection diagram of hydraulic motor (See Fig. 32)

Motor wires (M1、M2、M3) are connected to the three wires in the motor.

Turn on the power, push UP button, if motor run but lift is not worked, please. change the wires connection.

3.3  380V Circuit diagram (See Fig. 33)

Circuit diagram component list for 380V Power

| Item | Name | Code | Specification |  | Item | Name | Code | Specification |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | Power Switch | QS | 380V AC |  | 7 | Alarm Lamp | R | 220V (White) |
| 2 | Fuse | FU1 | 25A |  | 8 | Push Button | Down | Single |
| 3 | Fuse | FU2 | 3A |  | 9 | Motor | M | Three phases |
| 4 | AC Contactor | KM | 24V AC |  | 10 | Transformer | TC | 24V AC |
| 5 | Hydraulic Solenoid Valve | Y | 24V AC |  | 11 | Limit Switch | SQ | 10A |
| 6 | Push Button | UP | Single |  |  |  |  |  |

4.  220V Wire connection and circuit diagram

4.1 Wire Connection diagram in the control box (See Fig. 34)

4.2  220V Wire connection of hydraulic power unit (See Fig. 35).

Motor wires (M1、M2) are separately connected to two wires in the motor

  - 220V Circuit diagram (See Fig. 36).

Circuit diagram component list for 220V Power

| Item | Name | Code | Specification |  | Item | Name | Code | Specification |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | Power Switch | QS | 380V AC |  | 7 | Alarm Lamp | R | 220V (White) |
| 2 | Fuse | FU1 | 25A |  | 8 | Push Button | Down | Single |
| 3 | Fuse | FU2 | 3A |  | 9 | Motor | M | Single phase |
| 4 | AC Contactor | KM | 24V AC |  | 10 | Transformer | TC | 24V AC |
| 5 | Hydraulic Solenoid Valve | Y | 24V AC |  | 11 | Limit Switch | SQ | 10A |
| 6 | Push Button | Single | Black |  |  |  |  |  |

O. Install Retainer, Protective cover and Safety Cover.

1. Make sure the installation position of the oil hose, safety cable, wire cable before install retainers (See Fig. 37, 38).

Note: Don’t cross the oil hose and safety cable together

2. Install retainer (See Fig. 39).

3. Install Protective cover and safety cover.

a. Install protective cover of powerside column (See Fig. 40, 41).

b. The same way to install protective cover of offside column, only offside oil hose inside the protective cover.

c. Install protective cover for high setting (See Fig. 42).

Note: No need to install the shortest protective cover for low setting

P. Install lifting arms and adjust the arm locks.

1. Install the lifting arms (See Fig. 43).

2. Lowing the carriages down to the lowest position, then use the 8# socket head wrench to loosen the socket bolt (See Fig. 44).

3. Adjust the arm lock as direction of arrow (See Fig. 45)

4. Adjust moon gear and arm lock to make it to be meshed, then tighten the socket bolts of arm lock (See Fig.46).

IV. EXPLODED VIEW

Model A204C A240CH

Cylinders

Control Box

SPX ELECTRIC POWER UNIT 220V/50HZ/1 phase

PEAK ELECTRIC POWER UNIT

Illustration of hydraulic valve for SPX & PEAK hydraulic power unit

- SPX Electric power unit, 220V/50HZ, Single phase (See Fig. 52)

b. PEAK Electric power unit, 220V/50HZ/ 1 phase (See Fig. 53)

C. PEAK Electric power unit, 380V/50HZ/3 phases (See Fig. 54)

V. TEST RUN

1. Adjust synchronous cable (See Fig. 55)

Use wrench to hold the cable fitting, meanwhile

use ratchet spanner to tighten the cable nut.

Make sure two cables are with the same tension

so that two carriage can work synchronously.

Fit the plastic hole cover on the lifting head.

If the carriage does not Synchronize when lifting,

please tighten the cable nut of lower side carriage.

2. Adjust safety cable

Lifting the carriage and lock at the same height, strain the Safety Cable and then release a little, and then tighten the cable nuts. Make sure the safety device can always be worked properly. And then install the safety cover.

3. Bleeding air

This hydraulic system is designed to bleeding air by loosing

the bleeding plug. Lifting the carriages to about 1 meter

height, and loose the bleeding plug, the air would be

bled automatically, then tighten the plug after

bleeding, the lift would work stably and smoothly,

otherwise repeat bleeding (See Fig. 56).

4. Adjust the lower speed (Only for PEAK power unit)

You can adjust the lower speed of the lift if needing: Loosen the fixing nut of the throttle valve, and then turn the throttle valve clockwise to decrease the lower speed, or counterclockwise to increase the lower speed. Do not forget to tighten the fixing nut after the lower speed adjustment has been done.

4. Test with load

After finishing the above adjustment, test running the lift with load. Run the lift in low position for several times first, make sure the lift can rise and lower synchronously,  the Safety Device can lock and release synchronously. And then test run the lift to the top completely. If there are anything improper, repeat the above adjustment.

NOTE: It may be vibrated when lifting at start, please lifting it with load for several times, the air would be bled and the vibration would be disappeared automatically.

VI. OPERATION INSTRUCTIONS

Please read the safety tips carefully before operating the lift

To lift vehicle

- Keep clean of site near the lift;

- Position lift arms to the lowest position;

- To shortest lift arms;

- Open lift arms;

- Position vehicle between columns;

- Move arms to the vehicle’s lifting point;

Note: The four lift arms must at the same time contact the vehicle’s lifting point where manufacturers recommended

- Turn on the power switch QS1, press the UP button until the lift pads contact underside of vehicle totally. Recheck to make sure vehicle is secure;

- Continue to raise the lift slowly to the desired working height , ensuring the balance of vehicle;

- Press DOWN button, lower lift onto the safety position. The vehicle is ready to repair.

To lower vehicle

- Be sure clear of around and under the lift, only leaving operator in lift area;

- Press the UP button to raise the vehicle slightly, and then release the safety device, press the button DOWN to lower lift.

- Open the arms and position them to the shortest length;

- Drive away the vehicle.

- Turn off the power.

VII.MAINTENANCE SCHEDULE

Monthly:

- Re-torque the anchor bolts to 117 Nm;

- Check all connectors, bolts and pins to insure proper mounting;

- Lubricate cable with lubricant;

- Make a visual inspection of all hydraulic hoses/lines for possible wear or leakage;

- Check safety device and make sure proper condition;

- Lubricate all rollers and pins with 90wt. Gear oil or equivalent;

Note: All anchor bolts should take full torque. If any of the bolts does not function for any reason, DO NOT use the lift until the bolt has been replaced.

Every six months:

- Make a visual inspection of all moving parts for possible wear, interference or damage.

- Check and adjust as necessary, equalizer tension of the cables to insure level lifting.

- Check columns for plumbness.

- Check rubber pads and replace as necessary.

- Check safety device and make sure proper condition.

VIII.TROUBLE SHOOTING

| TROUBLE | CAUSE | REMEDY |
| --- | --- | --- |
| Motor does not run | 1. Button does not work 2. Wiring connections are not in good condition 3. Motor burned out 4. AC contactor burned out 5. Height limit switch is damaged | 1. Replace button 2. Repair all wiring connections 3. Repair or replace motor 4. Replace AC contactor 5. Replace the limit switch |
| Motor runs but the lift is not raised | 1. Motor runs in reverse rotation 2. Gear Pump out of operation 3. Release Valve in damage 4. Relief valve or check valve in damage 5. Low oil level | 1.Reverse two power wire 2.Repair or replace 3.Repair or Replace 4.Repair or replace 5.Fill tank |
| Lift does not stay up | 1. Release valve out of work 2. Relief valve or check valve leakage 3. Cylinder or fittings leaks | Repair or replace |
| Lift raises slowly | 1. Oil line is jammed 2. Motor running on low voltage 3. Oil mixed with air 4. Gear Pump leaks 5. Overload lifting | 1. Clean the oil line 2. Check electrical system 3. Fill tank 4. Repair or replace 5. Check load |
| Lift can not lower | 1. Safety device are in activated 2. Release valve in damage 3. Safety cable broken 4. Oil system is jammed 5. Hydraulic solenoid valve out of work | 1. Release the safeties 2. Repair or replace 3. replace 4. Clean the oil system 5. Repair or replace |

IX. PARTS LIST FOR A240C and A240CH

| Item | Part# | Description | Qty. | Note |
| --- | --- | --- | --- | --- |
|  |  |  | A240C | A240CH |  |
| (See Fig. 47, Fig.16, 23-29, Fig. 9) |
| 1 | 206019 | Snap Ring | 6 | 6 |  |
| 2 | 206058 | Bolt | 2 | 2 |  |
| 3 | 206059 | Washer | 2 | 2 |  |
| 4 | 209057B | Bronze Bush For Pulley | 6 | 6 |  |
| 5 | 206020 | Pulley | 6 | 6 |  |
| 6 | 206122 | Powerside Column | 1 | 1 |  |
| 200 | 420019 | Electric Power Unit | 1 | 1 |  |
| 7 | 209003 | Hex Bolt | 8 | 8 |  |
| 8 | 209004 | Rubber Ring | 4 | 4 |  |
| 9 | 209005 | Nylok Nut | 8 | 8 |  |
| 10 | 206002 | Safety Pin | 2 | 2 |  |
| 11 | 209007A | Safety Spring | 2 | 2 |  |
| 12 | 206003 | Handle Protective Plastic cushion | 1 | 1 |  |
| 13 | 206004 | Powerside Safety Lock | 1 | 1 |  |
| 14 | 209012 | Hair Pin | 2 | 2 |  |
| 15 | 206006 | Washer | 24 | 24 |  |
| 16 | 206023A | Hex Nut | 2 | 2 |  |
| 17 | 206004A | Safety Pulley Bracket | 1 | 1 |  |
| 18 | 209009 | Cup Head Bolt | 10 | 10 |  |
| 19 | 206081 | Safety Cover | 2 | 2 |  |
| 20 | 420045 | Washer | 16 | 16 |  |
| 20A | 209149 | Lock washer | 6 | 6 |  |
| 21 | 209022 | Washer | 40 | 40 |  |
| 22 | 209021 | Hex nut | 20 | 20 |  |
| 23 | 206010 | Safety Pulley Bracket | 1 | 1 |  |
| 24 | 206009 | Plastic Small Pulley | 5 | 5 |  |
| 25 | 209010 | Snap Ring | 5 | 5 |  |
| 26 | 209033 | Washer | 8 | 8 |  |
| 27 | 206008 | Extension Column | 2 | 0 |  |
|  | 206082 |  | 0 | 2 |  |
| 28 | 206015C | Wire Cable | 1 | 0 |  |
|  | 206015D |  | 0 | 1 |  |
| 29 | 209111 | Protective Ring For Cylinder | 2 | 2 |  |
| 30 | 217056 | Hydraulic Cylinder | 2 | 2 |  |

| Item | Part# | Description | Qty. | Note |
| --- | --- | --- | --- | --- |
|  |  |  | A240C | A240CH |  |
| 31 | 206044 | Slider Block | 16 | 16 |  |
| 32 | 206046A | Arm Lock Bar（left） | 4 | 4 |  |
| 33 | 206050A | Spring | 4 | 4 |  |
| 34 | 217044 | Arm Lock | 4 | 4 |  |
| 35 | 206032 | Snap Ring | 4 | 4 |  |
| 36 | 206036 | Hair Pin | 4 | 4 |  |
| 37 | 209016 | Carriage Plastic Cover | 2 | 2 |  |
| 38 | 206046B | Arm Lock Bar（right） | 2 | 2 |  |
| 39 | 206136 | Arm Pin | 4 | 4 |  |
| 40 | 206048 | Socket Bolt | 12 | 12 |  |
| 41 | 206049 | Moon Gear | 4 | 4 |  |
| 42 | 209019 | Screw | 12 | 12 |  |
| 43 | 209018 | Protective Rubber | 2 | 2 |  |
| 44 | 206111 | Carriage | 2 | 2 |  |
| 45 | 206053 | Lifting Arm – Front Right | 1 | 1 |  |
| 45A | 206087A | Outer Arm - Front Right | 1 | 1 |  |
| 45B | 206088 | Middle Arm - Front Right | 1 | 1 |  |
| 45C | 206095 | Inner Arm - Front Right | 1 | 1 |  |
| 46 | 206055 | Lifting Arm - Front Left | 1 | 1 |  |
| 46A | 206092A | Outer Arm - Front Left | 1 | 1 |  |
| 46B | 206093 | Middle Arm - Front Left | 1 | 1 |  |
| 46C | 206095 | Inner Arm - Front Left | 1 | 1 |  |
| 47 | 206039 | Lifting Arm – Rear Left | 1 | 1 |  |
| 47A | 206094A | Outer Arm - Rear Left | 1 | 1 |  |
| 47B | 206096 | Inner Arm - Rear Left | 1 | 1 |  |
| 48 | 209039 | Lock washer | 40 | 40 |  |
| 49 | 209038 | Hex bolt | 6 | 6 |  |
| 50 | 206037 | Lifting Arm - Rear Right | 1 | 1 |  |
| 50A | 206090A | Outer Arm - Rear Right | 1 | 1 |  |
| 50B | 206096 | Inner Arm - Rear Right | 1 | 1 |  |
| 51 | 203054 | Rubber Pad Assy. | 4 | 4 |  |
| 51A | 201060 | O Ring | 8 | 8 |  |
| 51B | 203024 | Adjustment Adapter | 4 | 4 |  |
| 51C | 203042 | Lock washer | 8 | 8 |  |
| 51D | 203025 | Adjustment Screw | 4 | 4 |  |
| 51E | 203041 | Lock washer | 4 | 4 |  |
| 52A | 203026 | Rubber Pad Frame | 4 | 4 |  |
| Item | Part# | Description | Qty. | Note |
|  |  |  | A240C | A240CH |  |
| 52B | 203043 | Rubber pad for Combined Adapter | 4 | 4 |  |
| 52C | 420043 | Socket bolt | 8 | 8 |  |
| 53 | 206025A | Foam Cushion | 1 | 1 |  |
| 54 | 201005 | Split Pin | 2 | 2 |  |
| 55 | 206129 | Control Bar | 1 | 1 |  |
| 56 | 206025C | Connecting Pin for Control Bar | 2 | 2 |  |
| 57 | 206013 | Limit Switch | 2 | 2 |  |
| 58 | 206011 | Cup Head Bolt | 2 | 2 |  |
| 59 | 206042 | Control Bar Support Bracket | 2 | 2 |  |
| 60 | 206041 | Hex Bolt | 4 | 4 |  |
| 61 | 206023 | Nylok Nut | 12 | 12 |  |
| 62 | 206017 | Hex Bolt | 28 | 28 |  |
| 62A | 209056 | Nylok nut | 10 | 10 |  |
| 63 | 206016 | Connecting Bracket | 1 | 1 |  |
| 64 | 206018A | Top Beam W/Bracket | 2 | 2 |  |
| 65 | 206028 | Cup Head Bolt | 4 | 4 |  |
| 66 | 206029 | Retainer | 2 | 2 |  |
| 67 | 206021 | Pin For Pulley | 2 | 2 |  |
| 68 | 206022 | Pin Spacer | 2 | 2 |  |
| 69 | 206024 | Hex Bolt | 8 | 8 |  |
| 70 | 206010A | Safety Pulley Bracket | 1 | 1 |  |
| 71A | 206110 | Cup Head Bolt | 6 | 6 |  |
| 71 | 206085 | Protective cover | 2 | 2 |  |
| 72 | 206084 | Protective cover | 2 | 2 |  |
| 73 | 206083 | Protective cover | 2 | 2 |  |
| 74 | 640050 | Socket bolt | 4 | 4 |  |
| 75 | 206008C | Safety Pulley Bracket | 1 | 1 |  |
| 76 | 206026 | Offside Safety Lock | 1 | 1 |  |
| 77 | 217048 | Retainer | 2 | 2 |  |
| 78 | 206079 | Cup Head Bolt | 20 | 20 |  |
| 79 | 206080 | Protective cover | 2 | 2 |  |
| 80 | 206030B | Offside column | 1 | 1 |  |
| 80A | 203034 | Adapter 3” | 4 | 4 |  |
| 81 | 209059 | Anchor Bolt | 10 | 10 |  |
| 82 | 620065 | Shim | 10 | 10 |  |
| 83 | 209066 | Cable Nut | 8 | 8 |  |
| Item | Part# | Description | Qty. | Note |
|  |  |  | A240C | A240CH |  |
| 84 | 206064A | Cable | 2 | 0 |  |
|  | 206064B |  | 0 | 2 |  |
| 85 | 206065 | Safety Cable | 1 | 0 |  |
|  | 206065A |  | 0 | 1 |  |
| 86 | 203032 | Motor Bracket | 1 | 1 |  |
| 87 | 206134 | Oil Hose | 1 | 0 |  |
|  | 206135 | Oil Hose | 0 | 1 |  |
| 88 | 209060 | 90 Fitting For Power Unit | 1 | 1 |  |
| 88A | 211016 | T- Fitting | 1 | 1 |  |
| 89 | 209064 | Straight Fitting | 2 | 2 |  |
| 90 | 206062 | Straight Fitting | 2 | 2 |  |
| 91 | 233009 | Pipe Fitting | 2 | 2 |  |
| 92 | 206130 | Oil Hose | 2 | 0 |  |
|  | 206131 |  | 0 | 2 |  |
| 93 | 206123 | Control Box | 1 | 1 |  |
| 94 | 209145 | Cup Head Bolt | 2 | 2 |  |
| 95 | 206120 | Wire cable | 1 | 0 |  |
|  | 206121 | Wire cable | 0 | 1 |  |
| 96 | 620095 | Hex Nut | 4 | 4 |  |
| 97 | 620109 | Cup head bolt | 2 | 2 |  |
| 98 | 420164 | Cup head bolt | 2 | 2 |  |
| 99 | 209126 | Hex Nut | 2 | 2 |  |
| 100 | 420168A | White bobbin | 1 | 1 |  |
| 101 | 206116 | Wire for Hydraulic Solenoid Valve | 1 | 1 |  |
| 102 | 206139 | Motor Wire | 1 | 1 |  |
| 103 | 206114 | Protecting plastic hose | 1 | 0 |  |
|  | 206115 | Protecting plastic hose | 0 | 1 |  |
| 104 | 209152 | Ties | 3 | 3 |  |
| 105 | 217145 | Plastic clamp | 3 | 3 |  |
| 106 | 520023 | Snap Ring | 4 | 4 |  |
| 107 | 206502B | Parts Box | 1 | 0 |  |
|  | 206503B |  | 0 | 1 |  |
| Parts For Hydraulic Cylinder (See Fig.48) |
| 30-1 | 209069 | O-Ring | 2 | 2 |  |
| 30-2 | 209070 | Bleeding Plug | 2 | 2 |  |
| 30-3 | 209071 | Support Ring | 2 | 2 |  |
| Item | Part# | Description | Qty. | Note |
|  |  |  | A240C | A240CH |  |
| 30-4 | 209072 | Y-Ring | 2 | 2 |  |
| 30-5 | 209073 | O-Ring | 2 | 2 |  |
| 30-6 | 209074 | Piston | 2 | 2 |  |
| 30-7 | 209075 | O-Ring | 2 | 2 |  |
| 30-8 | 217076 | Piston Rod | 2 | 2 |  |
| 30-9 | 209077 | Piston Rod Fitting | 2 | 2 |  |
| 30-10 | 209078 | Dust Ring | 2 | 2 |  |
| 30-11 | 209079 | Head Cap | 2 | 2 |  |
| 30-12 | 209080 | O-Ring | 2 | 2 |  |
| 30-13 | 209081A | Bore Weldment | 2 | 2 |  |
| Part for Control Box (See Fig.49) |
| 93-1 | 420069A | Cover Of Control Box | 1 | 1 |  |
| 93-2 | 61K077 | Alarm Lamp | 1 | 1 |  |
| 93-3 | 420071 | Button UP | 1 | 1 |  |
| 93-4 | 420072 | Button DOWN | 1 | 1 |  |
| 93-5 | 420139 | Screw | 4 | 4 |  |
| 93-6 | 420074 | Power Switch (QSI) | 1 | 1 |  |
| 93-7 | 420085 | Fuse Cap | 3 | 3 |  |
| 93-8 | 420086 | Fuse (FU1) | 3 | 3 |  |
| 93-9 | 420087 | Fuse Base | 3 | 3 |  |
| 93-10 | 620082 | 15 digits Terminal Group | 1 | 1 |  |
| 93-11 | 420133A | Panel for Installing Element | 1 | 1 |  |
| 93-12 | 420073 | Cup Head Bolt | 4 | 4 |  |
| 93-13 | 420140 | Thermal Relay (FR) | 1 | 1 |  |
| 93-14 | 420134 | Transformer (TC) | 1 | 1 |  |
| 93-15 | 420084A | 24V AC Contactor (KM) | 1 | 1 |  |
| 93-16 | 420088 | Fitting For White Wire Cable | 3 | 3 |  |
| Parts For SPX Electric Power Unit 220V/50HZ/1 Phase (See Fig.50) |
| 200-1 | 209082 | Motor | 1 | 1 |  |
| 200-2 | 209083 | Motor Connecting Shaft | 1 | 1 |  |
| 200-3 | 209084 | Valve Body | 1 | 1 |  |
| 200-4 | 209085 | Relief Valve | 1 | 1 |  |
| 200-5 | 209086 | Lock Washer | 4 | 4 |  |
| 200-6 | 209087 | Socket Bolt | 4 | 4 |  |
| 200-7 | 209088 | Inlet Pipe | 1 | 1 |  |
| 200-8 | 209089 | O-ring | 1 | 1 |  |
| Item | Part# | Description | Qty. | Note |
|  |  |  | A240C | A240CH |  |
| 200-9 | 209090 | Filter | 1 | 1 |  |
| 200-10 | 209091 | Hex Bolt | 4 | 4 |  |
| 200-11 | 209092 | Reservoir | 1 | 1 |  |
| 200-12 | 209093 | Cup Head Bolt | 2 | 2 |  |
| 200-13 | 209094 | Cover for Capacitor | 1 | 1 |  |
| 200-14 | 209095 | Capacitor | 1 | 1 |  |
| 200-15 | 209096 | Rubber Gasket | 1 | 1 |  |
| 200-16 | 209097 | Hex Bolt | 1 | 1 |  |
| 200-17 | 209098 | Cover of Motor Terminal Box | 1 | 1 |  |
| 200-18 | 209110 | Oil Return Port | 1 | 1 |  |
| 200-19 | 209100 | Oil Outlet | 1 | 1 |  |
| 200-20 | 209162 | Hydraulic Solenoid Valve Nut | 1 | 1 |  |
| 200-21 | 209115 | Hydraulic Solenoid Valve Coil | 1 | 1 |  |
| 200-22 | 209116 | Hydraulic Solenoid Valve Body | 1 | 1 |  |
| 200-23 | 209117 | Pressure Adjusting Bar | 1 | 1 |  |
| 200-24 | 420070 | Check Valve | 1 | 1 |  |
| 200-25 | 209106 | Gear Pump | 1 | 1 |  |
| 200-26 | 209107 | Oil Return Pipe | 1 | 1 |  |
| 200-27 | 209108 | Filler Cap | 1 | 1 |  |
| Parts For PEAK Electric Power Unit 220V/50HZ/1 Phase (See Fig.51) |
| 200A-1 | 209082A | Motor | 1 | 1 |  |
| 200A-2 | 209083A | Motor Connecting Shaft | 1 | 1 |  |
| 200A-3 | 209084A | Valve Body | 1 | 1 |  |
| 200A-4 | 209085A | Relief Valve | 1 | 1 |  |
| 200A-5 | 209113 | Throttle Valve | 1 | 1 |  |
| 200A-6 | 209086A | Lock Washer | 4 | 4 |  |
| 200A-7 | 209087A | Socket Bolt | 4 | 4 |  |
| 200A-8 | 209088A | Inlet Pipe | 1 | 1 |  |
| 200A-9 | 209089A | O-ring | 1 | 1 |  |
| 200A-10 | 209090A | Filter | 1 | 1 |  |
| 200A-11 | 209091A | Hex Bolt | 4 | 4 |  |
| 200A-12 | 209092A | Reservoir | 1 | 1 |  |
| 200A-13 | 209093A | Cup Head Bolt | 4 | 4 |  |
| 200A-14 | 209094A | Cover for Capacitor | 2 | 2 |  |
| 200A-15 | 209095A | Start Capacitor | 1 | 1 |  |
| 200A-15A | 209095B | Run Capacitor | 1 | 1 |  |
| Item | Part# | Description | Qty. | Note |
|  |  |  | A240C | A240CH |  |
| 200A-16 | 209096A | Rubber Gasket | 2 | 2 |  |
| 200A-17 | 209097A | Hex Bolt | 2 | 2 |  |
| 200A-18 | 209098A | Cover of Motor Terminal Box | 1 | 1 |  |
| 200A-19 | 209110A | Oil Return Port | 1 | 1 |  |
| 200A-20 | 209100A | Oil Outlet | 1 | 1 |  |
| 200A-21 | 420070A | Check Valve | 1 | 1 |  |
| 200A-22 | 209162A | Hydraulic Solenoid Valve Nut | 1 | 1 |  |
| 200A-23 | 209115A | Hydraulic Solenoid Valve Coil | 1 | 1 |  |
| 200A-24 | 209116A | Hydraulic Solenoid Valve Body | 1 | 1 |  |
| 200A-25 | 209117A | Pressure Adjusting Bar | 1 | 1 |  |
| 200A-26 | 209106A | Gear Pump | 1 | 1 |  |
| 200A-27 | 209107A | Oil Return Pipe | 1 | 1 |  |
| 200A-28 | 209108A | Filler Cap | 1 | 1 |  |
| Parts For PEAK Electric Power Unit 380V/50HZ/3 Phase ( See Fig.51) |
| 200B-1 | 209118 | Motor | 1 | 1 |  |
| 200B-2 | 209083A | Motor Connecting Shaft | 1 | 1 |  |
| 200B-3 | 209084A | Valve Body | 1 | 1 |  |
| 200B-4 | 209085A | Relief Valve | 1 | 1 |  |
| 200B-5 | 209113 | Throttle Valve | 1 | 1 |  |
| 200B-6 | 209086A | Lock Washer | 4 | 4 |  |
| 200B-7 | 209087A | Socket Bolt | 4 | 4 |  |
| 200B-8 | 209088A | Inlet Pipe | 1 | 1 |  |
| 200B-9 | 209089A | O-ring | 1 | 1 |  |
| 200B-10 | 209090A | Filter | 1 | 1 |  |
| 200B-11 | 209091A | Hex Bolt | 4 | 4 |  |
| 200B-12 | 209092A | Reservoir | 1 | 1 |  |
| 200B-13 | 209097A | Hex Bolt | 2 | 2 |  |
| 200B-14 | 209098A | Cover of Motor Terminal Box | 1 | 1 |  |
| 200B-15 | 209110A | Oil Return Port | 1 | 1 |  |
| 200B-16 | 209100A | Oil Outlet | 1 | 1 |  |
| 200B-17 | 420070A | Check Valve | 1 | 1 |  |
| 200B-18 | 209162A | Hydraulic Solenoid Valve Nut | 1 | 1 |  |
| 200B-19 | 209115A | Hydraulic Solenoid Valve Coil | 1 | 1 |  |
| 200B-20 | 209116A | Hydraulic Solenoid Valve Body | 1 | 1 |  |
| 200B-21 | 209117A | Pressure Adjusting Bar | 1 | 1 |  |
| 200B-22 | 209106A | Gear Pump | 1 | 1 |  |
| 200B-23 | 209107A | Oil Return Pipe | 1 | 1 |  |
| 200B-24 | 209108A | Filler Cap | 1 | 1 |  |

# Text boxes

TWO-POST LIFT

Model:A240C A240CH

Fig. 1

1350mm

893mm

2528mm

722mm

1285mm

Fig. 2

Fig. 3

Fig. 4

81

Concrete intensity must be 3000psi minimum

100

Model A240C A240CH

Chalk Line

Fig. 5

Fig. 6

Parts box

Aluminum name plate

Extension Column

(Outer Column)

Lifting Arm

Top Connecting Assy.

Shipment Parts list

Fig.7

Fig.8

107

Fig. 9

Fig.10

Model A240C A240CH

Fig. 11

Fig. 12

The install direction of the plastic pulley

Fig. 13

44

44

Fig. 15 High Setting

Fig. 14 Low Setting

6

27

80

Width between Columns:2850mm

Check the column plumbness with lever bar from front, aside, make sure they are vertical

81

82

Overall width：3428mm

Install the anchor bolts

Note:Minimum embedment of Anchors is 90mm.

90mm

Fig. 16

Drilling

Bolting

Tighten

63

62

62A

61

15

69

64

Fig. 17

64

Tighten the anchor bolts with ratchet spanner with socket. Note: Torque of  Anchors is 117N.m.

Fig. 18

96

View A

103

104

105

97

95

57

98

30º

Cylinder limit switch

4#

5#

Control bar

Control bar Limit Switch

3#

2#

Control bar Limit Switch

61

View A

Install cylinder limit switch

30º

NC: Normal contact

Fig. 19

Bending here

Powerside Safety Device

Fig. 20

Offside Safety Device

Fig. 21

Safety block lock at the same level

Fig. 22

Low Setting

Cable 2

Cable 1

83

Cable 2

84

Fig. 23

High Setting

Screw the two cable nuts

Cable pass through the cable fixing plate in carriages

Cable Connecting direction

Cable connecting direction

Fig. 24

Cable 2

Cable 1

83

84

Cable 2

Fig. 25

View A

Tighten the nut after finishing  installation of safety cable

View B

Assemble safety cable from offside safety assy.

Fig. 26

99

21

62A

86

200

9

8

7

89

87

88

30

92

90

91

88A

92

Fig. 27

20A

20

94

93

Fig. 28

Connecting wire of hydraulic Solenoid Valve

Connecting wire of control bar limit switch

Connecting the power wire

100

101

102

Connecting wire cylinder limit switch

Connecting wire of motor

Fig. 29

Using cross screwdriver to adjust rated current value of thermal relay

This point shows the present rated current value

Fig. 30

Wire of motor

Wire of  control bar limit switch

Wire of hydraulic solenoid valve

Power wire

Earth wire

Wire of  cylinder limit switch

Fig. 31

Earth wire

M3

M2

M1

Fig. 32

Fig. 33

3 Phases

Earth wire

Wire of  cylinder limit switch

Wire of motor

Power wire

Wire of  control bar limit switch

Wire of hydraulic solenoid valve

Fig. 34

Earth wire

M2

M1

Fig. 35

Single phase

Fig. 36

Fig. 36

Safety Cable

Oil hose

Wire of cylinder limit switch

Wire of control bar limit switch

Off powerside

Fig. 38

Powerside

Fig. 37

65

66

Safety Cable

Safety Cable

Oil Hose

Oil Hose

Safety cable can’t not pass through the retainer

Wire of limit switch

Fig. 39

No need the shortest Protective cover for low setting

18

77

Powerside oil hose

Fig. 41

Fig. 40

Safety Cable

- Install protective cover and tighten the cup head bolt

- Screw the head cup bolt M6*40

Wire  of cylinder limit switch

Power unit oil hose

Wire of hydraulic solenoid valve

Wire of motor

Cylinder oil hose

Wind the white bobbin

Wire of control bar limit switch

Wind the white bobbin

Fig. 42

Snap Ring

Fig. 43

use the 8# socket head wrench to loosen the socket bolt

Fig. 44

Arm lock

Fig. 45

Locking the bolts after the moon gear and arm lock engaged well

Fig. 46

Car in direction

Fig.47

Fig. 48

Fig. 49

Fig. 50

380V/50HZ/3 Phases

220V/50HZ/1 Phase

Fig. 51

Capacitor

Oil return port

Auxiliary hole

Oil Outlet

Solenoid valve

Check valve

Relief valve

Auxiliary hole

Fig. 52

Fig. 53

Fig. 54

Cable nut

Fig. 55

Bleeding plug

Fig. 56

Throttle Valve

Fixing Nut

Counterclockwise to increase the  down speed

Clockwise to decrease the  down speed

Fig. 57

Fig. 58 Hydraulic System

72225402

01/2014