CONTENTS

Product Features and Specifications ........................................................... 1

Installation Requirement .......................................................................... 2

Steps of Installation…………………………………………………………………………………………….. 4

Exploded View .......................................................................................13

Test Run................................................................................................18

Operation Instruction ..............................................................................19

Maintenance ..........................................................................................19

Trouble Shooting ....................................................................................20

Parts List ..............................................................................................21

I. PRODUCT FEATURES AND SPECIFICATIONS (See Fig.1)

FLUSH-MOUNT SCISSORS MODEL SX08F

· Electric/Hydraulic power system.

· Dual cylinders automatic synchronization system.

· Safety self-lock mechanism.

· Extended platforms.

MODEL SX08F SPECIFICATIONS

| Model | Lifting Capacity | Lifting Height | Min. Height | Lifting Time | Overall Length | Runway Width | Width Between Bases | Gross Weight | Motor |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| SX08F | 3.5T 8,000lbs | 2230mm 87 7/8” | 350mm 13 3/4” | 51S | 1540-1740mm 60 5/8”-68 1/2” | 550mm 21 5/8” | 800mm 31 1/2” | 822Kg 1,800lbs | 2.0/3.0 HP |

II. INSTALLATION REQUIREMENT

A. TOOLS REQUIRED

  - Rotary Hammer Drill

(Φ19、Φ10、Φ4)

  - Hammer

  - Level Bar

  - English Spanner (12")

  - Wrench set ( 15#, 17#)

  - Carpenter’s Chalk

  - Screw Sets

  - Tape Measure (7.5m)

  - Pliers

(  Lock Wrench

(   Grease gun

(   Ratchet Spanner with Socket

B. SPECIFICATIONS OF CONCRETE

Specifications of concrete must be adhere to the specifications as following. Failure to do so may result in lift and/or vehicle falling.

- Lift Location: Always use architect plans when available. Check layout dimension

against floor plan requirements making sure that adequate space is available.

2. Overhead Obstructions: The area where the lift will be located should be free of overhead obstructions such as heaters, building supports, electrical lines etc.

3. Concrete: Visually inspect the site where the lift is to be installed and check for cracked or defective concrete. All models must be installed on 3000psi（210kg/cm2）minimum. Concrete with a thickness 100mm and without reinforcing steel bars.

C. POWER SUPPLY

The electrical source must be 2.2KW minimum. The source cable size must be 2.5mm² and in good condition of contacting with floor.

WARNING !

A level floor is suggested for proper installation and level adjustment. Small differences in floor slopes may be compensated by shim. If a floor is of questionable slope, consider pouring a new concrete slab.

- DO NOT install this lift on any asphalt surface or any surface other ground than

concrete.

- DO NOT install this lift on expansion seams or on cracked or defective concrete.

- DO NOT install this lift on a second/elevated floor without first consulting build

architect.

- DO NOT install this lift outdoors unless special consideration has been made to protect the power unit from weather conditions.

III. STEPS OF INSTALLATION

- Location of installation (See Fig. 3)

Review the layout as shown below and select a location that is best suited for your application. Be sure to use the dimensions that are applicable to your lift model.

Note: 1. Concrete must be thickness 100mm minimum and must be of test strength 3,000psi (210kg/cm²) minimum.

2. All the tubes must be (50 PVC tube.

- The electrical source must be 380V. The source cable size must be 4×2.5mm².

B. Check the parts before assembly, make sure all the parts are completed.

- Packaged lift, parts box, control cabinet (See Fig.4).

- Move the parts aside, open the outer packing and check the parts according to the shipment parts list (See Fig. 5).

3. Open the parts box, check the parts according to the part list (See Fig. 6).

4. Check the parts of the parts bag according to the parts bag list (See Fig. 7).

C. Layout the machine and install oil system and air line system.

1. Select a location and layout the equipment according to steps B (See Fig. 8).

2. Connecting the oil hose and air line (See Fig. 9).

3. Install the oil-water separator (See Fig. 10).

D. Install electric system

1. Adjusting the current rating of thermal relay in control box according to the different configurations of hydraulic power unit. In general, the electric current of thermal relay should equal or larger than that of motor. The following table shows rated current regulation of thermal relay in case of different hydraulic power unit.

| Hydraulic power unit | Single phase | Three phase |
| --- | --- | --- |
| Rated current of thermal relay | 18A | 12A |

2. Wire connection for hydraulic power unit (for 3 phase)

2.1 Connect the power wire and limit switch wire according to the Wiring diagram (See Fig. 12).

2.2 Circuit Diagram (See Fig. 13).

| Item | Name | Code | Specification |  | Item | Name | Code | Specification |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | Power switch | QS | 380V AC |  | 10 | Push button | Up | Duplex |
| 2 | Fuse | FU1 | 25A |  | 11 | Push button | Lock | Duplex |
| 3 | Fuse | FU2 | 3A |  | 12 | Push button | Down1 | Trigeminy |
| 4 | AC contactor | KM | 24V AC |  | 13 | Push button | Down2 | Duplex |
| 5 | Thermal relay | FR | 12A-18A |  | 14 | Motor | M | 3 Phase |
| 6 | Time relay | KT | 24V AC |  | 15 | Buzzer | H | 24VAC |
| 7 | Limit switch | SQ(1~2) | 10A |  | 16 | Transformer | TC | 24V AC |
| 8 | Hydraulic solenoid valve | Y1 | AC 24V |  | 17 | Intermediate relay | KA | 24VAC |
| 9 | Air solenoid valve | Y2 | AC 24V |  |  |  |  |  |

Electric Component

3. Wire connection for hydraulic power unit (for single phase)

3.1 Connect the power wire and limit switch wire according to the Wiring diagram (See Fig. 14)

3.2 Circuit Diagram (See Fig. 15).

| Item | Name | Code | Specification |  | Item | Name | Code | Specification |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | Power switch | QS | 380V AC |  | 10 | Push button | Up | Duplex |
| 2 | Fuse | FU1 | 25A |  | 11 | Push button | LOCK | Duplex |
| 3 | Fuse | FU2 | 3A |  | 12 | Push button | Down1 | Trigeminy |
| 4 | AC contactor | KM | 24V AC |  | 13 | Push button | Down2 | Duplex |
| 5 | Thermal relay | FR | 12A-18A |  | 14 | Motor | M | Single phase |
| 6 | Time relay | KT | 24V AC |  | 15 | Buzzer | H | 24VAC |
| 7 | Limit switch | SQ(1~2) | 10A |  | 16 | Transformer | TC | 24V AC |
| 8 | Hydraulic solenoid valve | Y1 | 24V AC |  | 17 | Intermediate relay | KA | 24VAC |
| 9 | Air solenoid valve | Y2 | 24V AC |  |  |  |  |  |

Electric Component

E. Level two platforms and install anchor bolts.

1. Check by level bar and use the shim to adjust the platforms until two platforms are in the same level.

2. Install anchor bolts.

2.1 Raise the lift to 1000mm then drill holes to install the anchor bolts (See Fig.17).

2.2 Fix the Anchor bolts (3/4×5 1/2).

Drilling the hole for the anchor bolt with the rotary hammer drill, type the anchor bolt into the ground, and then fasten it with Ratchet spanner (See Fig. 18).

Note: The twisting force of anchor bolt is 117N.m, the length inside ground of anchor bolt must be over 90mm.

- Fix the control cabinet anchor bolts (M10×100mm) (See Fig. 19).

IV. EXPLODED VIEW

MODEL SX08F

CYLINDERS

CONTROL CABINET

SPX ELECTRIC POWER UNIT

220V/50HZ/1 Phase

PEAK ELECTRIC POWER UNIT (See Fig. 24)

Illustration of hydraulic valve for SPX & PEAK electric power unit

a. SPX Electric power unit, 220V/50HZ/1 phase (See Fig. 25)

b. PEAK Electric power unit, 220V/50HZ/1 phase (See Fig. 26)

c. PEAK Electric power unit, 380V/50HZ/3 phase (See Fig. 27)

V. TEST RUN

- Fill oil to cylinder

- Turn on the power, press the Up button, and check the rotated direction of the Motor. Exchange two source wire connection if the direction is reverse, and then follow the following procedure of filling oil to cylinders.

- Fill reservoir with Hydraulic Oil (Note: In consideration of power unit’s durability，please use Hydraulic Oil 46#).

- Press the button Down until the both platform down to the lowest position.

- Turn the Two-way valve to the position connected to the secondly cylinder, press the button Up and fill oil into the secondly cylinder till it is full, and then hold down the button Lock for a while for bleeding air. Repeating this operation until no air is in the hydraulic system (See Fig. 28).

- Turn the Two-way valve to the main cylinder, press the button Up to run the lift up and down for several times, meanwhile do the synchronous adjustment till the two safety device can lock and release at the same time (See Fig. 29).

B. Test run

Check the height limit switch, the hose and fitting connection, and do test run. The lift must be tested run and checked carefully before in use.

VI. OPERATION INSTRUCTIONS

To lift vehicle

- Keep clean of site near the lift, and down the lift to the lowest position.

- Drive vehicle to the platform and put on the brake.

- Turn on the power and press the button UP, raise the lift to the working position.

Note: make sure the vehicle is steady when the lift is rising

- Press the button Lock, lock the lift in the safe position. Make sure the safety is locked in the same height.

To lower vehicle

- Be sure clear of around and under the lift, only leaving operator in lift area.

- Press the button Down1, until the lift low down to 600mm from ground, low limit switch affect and the lift stop, then press Down1 and Down2, lift go on running down with warning alarm.

- Drive away the vehicle when the lift is lowered to the lowest position.

- Turn off the power.

VII.MAINTENANCE SCHEDULE

Monthly:

- Re-torque the anchor bolts to 80-117 Nm.

- Lubricate all moving parts with lubricant.

- Check all fittings, bolts and pins to insure proper mounting.

- Make a visual inspection of all hydraulic hoses/lines for possible wear or leakage.

- Adjusting the lifting level on both platform.

Note: All anchor bolts should take full torque. If any of the bolts does not function for any reason, DO NOT use the lift until the bolt has been replaced.

Every six months:

1. Make a visual inspection of all moving parts for possible wear, interference or damage.

2. Check and adjust the platform as necessary to insure level lifting.

3. Check all fastener and re-torque.

VIII.TROUBLE SHOOTING

| TROUBLE | CAUSE | REMEDY |
| --- | --- | --- |
| Motor does not run | 1.Button does not work 2. AC contactor burned out 3. Motor burned out | 1. Replace button 2. Replace AC contactor 3. Repair or replace motor |
| Motor have voice but not run | 1.Wiring connections of 3 phase are not in good condition. 2. AC contactor main contacts in poor contact | 1. Check the 3 phase wiring connections, and repair it if not in good condiction. 2. Replace AC contactor. |
| Motor runs but the lift is not raised | 1.Motor runs in reverse rotation 2.Low oil level 3.The Gear Pump out of operation 4.Relief valve or check valve in damage 5.Shaft Coupling in damage | 1.Reverse two power wire 2.Fill tank 3.Repair or replace 4.Repair or replace 5.Replace Shaft Coupling |
| Lift raised slowly | 1.Oil line is jammed 2. Gear Pump leaks 3.Overload lifting 4.Power Voltage low 5.Oil mixed with air | 1.Clean the oil line 2.Replace Pump 3.Check load 4.Check electrical system 5.Fill tank and bleeding air |
| Lift can not lower | 1. Hydraulic Solenoid valve out of operation 2. Low Air pressure can’t open the lock | 1. Check Solenoid valve and Air line 2.Adjusting Air pressure of Compressor |

IX. PARTS LIST FOR SX08F

| Item | Part# | Description | QTY. | Note |
| --- | --- | --- | --- | --- |
| (See Fig.20, Fig.9-10, Fig.18-19) |
| 1 | 610001A | Extended Platform | 2 |  |
| 2 | 610002A | Platform | 2 |  |
| 3 | 610003 | Slider for platform | 4 |  |
| 4 | 610098 | Snap Ring | 4 |  |
| 5 | 610005A | Cylinder Connecting Shaft | 2 |  |
| 6 | 610006A | Upper Scissor (Out) | 2 |  |
| 7 | 420138 | Socket Bolt | 4 |  |
| 8 | 610008 | Snap Ring | 16 |  |
| 9 | 610009 | Rotating Shaft B | 16 |  |
| 10 | 620064 | Greasing Fitting | 38 |  |
| 11 | 610011B | Upper Scissor (In) | 2 |  |
| 12 | 610012 | Washer | 20 |  |
| 13 | 610013A | Lower Scissor (Out) | 2 |  |
| 14 | 610014B | Lower Scissor (In) | 2 |  |
| 15 | 610095 | Hex Bolt | 8 |  |
| 16 | 610096 | Hex Nut | 8 |  |
| 17 | 610017A | Baseframe | 2 |  |
| 18 | 610018 | Rotating Shaft A | 8 |  |
| 19 | 610019 | Nylok Nut | 8 |  |
| 20 | 420153 | Cup Head Bolt | 8 |  |
| 21 | 520011 | Air Cylinder | 2 |  |
| 22 | 680005 | Cup Head Bolt | 4 |  |
| 23 | 610023 | Slider For Base | 4 |  |
| 23A | 610108 | Washer | 16 |  |
| 24 | 610024A | Safety Lock (Upper) | 2 |  |
| 24A | 610070 | Rubber Pad | 4 |  |
| 25 | 206011 | Cup Head Bolt | 4 |  |
| 26 | 610026 | Nylok Nut | 4 |  |
| 27 | 206013/ 610104 | Limit Switch assy | 1 |  |
| 27A | 420149 | Cup Head Bolt | 2 |  |
| 27B | 206013/ 610105 | Limit Switch assy | 1 |  |
| 27C | 61K053 | Cup Head Bolt | 2 |  |
| 27D | 620095 | Hex Nut | 4 |  |
| 28 | 610032A | Safety Lock Tube (Secondly) | 1 |  |
| 29 | 610031A | Secondly Cylinder | 1 |  |
| Item | Part# | Description | QTY. | Note |
| 30 | 610030A | Cylinder Pin | 2 |  |
| 30A | 520023 | Snap Ring | 4 |  |
| 31 | 610029A | Main Cylinder | 1 |  |
| 32 | 610028A | Safety Lock Tube (Main) | 1 |  |
| 33 | 610007A | Control Cabinet | 1 |  |
| 34 | 420047 | Fitting for Air Line | 2 |  |
| 35 | 520065 | Air Line (Spring) | 2 |  |
| 36 | 610060 | Air Line | 1 |  |
| 37 | 420124 | T-Fitting | 1 |  |
| 38 | 520069 | 90°Fitting For Air Line | 1 |  |
| 39 | 510023 | Straight Fitting For Cylinder | 2 |  |
| 40 | 201022 | T-Fitting For Cylinder | 1 |  |
| 41 | 610068 | Oil Hose（No.3） | 1 |  |
| 42 | 610066 | Oil Hose（No.1） | 1 |  |
| 43 | 610067 | Oil Hose（No.2） | 1 |  |
| 200 | 610037 | Electric Power Unit | 1 |  |
| 45 | 420076 | 90°Fitting For Air Line | 1 |  |
| 46 | 420145 | Oil Water Separator | 1 |  |
| 47 | 420146 | Air Line Fitting | 1 |  |
| 48 | 420018 | Nylok nut | 2 |  |
| 49 | 620065 | Shim | 20 |  |
| 50 | 209059 | Anchor Bolt | 8 |  |
| 51 | 620071 | Anchor Bolt | 4 |  |
| 52 | 440009 | Straight Fitting for Power Unit | 1 |  |
| 53 | 52K027 | 90° Fitting | 1 |  |
| 54 | 420097 | 90° Fitting | 2 |  |
| 55 | 61K018 | Two-way Valve | 1 |  |
| 56 | 610500 | Parts Box | 1 |  |
| Parts for Hydraulic Cylinder (See Fig. 21) |
| 31-1 | 610033 | Main Cylinder | 1 |  |
| 31-2 | 520053 | O- Ring | 1 |  |
| 31-3 | 520043 | Head Cap（Main） | 1 |  |
| 31-4 | 520052 | Support Ring | 1 |  |
| 31-5 | 520051 | Y- Ring | 1 |  |
| 31-6 | 520050 | Dust Ring | 1 |  |
| 31-7 | 610035 | Piston Rod (Main) | 1 |  |
| 31-8 | 520054 | O- Ring | 1 |  |
| 31-9 | 520055 | Y- Ring | 2 |  |

| Item | Part# | Description | QTY. | Note |
| --- | --- | --- | --- | --- |
| 31-10 | 520056 | Support Ring | 1 |  |
| 31-11 | 520045 | Piston (Main) | 1 |  |
| 31-12 | 520049 | Set Screw | 2 |  |
| 31-13 | 520047 | Hex Nut | 1 |  |
| 31-14 | 530009 | Hose Burst Valve | 2 |  |
| 29-1 | 610034 | Secondly Cylinder | 1 |  |
| 29-2 | 520060 | O- Ring | 1 |  |
| 29-3 | 520044 | Head Cap（Secondly） | 1 |  |
| 29-4 | 201034 | Bleeding Plug | 3 |  |
| 29-5 | 520058 | O- Ring | 1 |  |
| 29-6 | 520057 | Dust Ring | 1 |  |
| 29-7 | 610036 | Piston Rod (Secondly) | 1 |  |
| 29-8 | 520061 | O- Ring | 1 |  |
| 29-9 | 520062 | Support Ring | 1 |  |
| 29-10 | 520063 | Y- Ring | 1 |  |
| 29-11 | 520046 | Piston (Secondly) | 1 |  |
| 29-12 | 520049 | Set Screw | 1 |  |
| 29-13 | 520048 | Hex Nut | 1 |  |
| Parts for Control Cabinet (See Fig. 22) |
| 33-1 | 420071 | Button UP | 1 |  |
| 33-2 | 420071 | Button LOCK | 1 |  |
| 33-3 | 420072 | Button DOWN 1 | 1 |  |
| 33-4 | 420142 | Button DOWN 2 | 1 |  |
| 33-5 | 52K001B | Control Panel | 1 |  |
| 33-6 | 420074 | Power Switch (QS) | 1 |  |
| 33-7 | 52K007B | Cabinet Body | 1 |  |
| 33-8 | 420167C | Air Line | 1 |  |
| 33-9 | 61K110 | Straight Fitting For Air Line | 1 |  |
| 33-10 | 209145 | Cup Head Bolt | 4 |  |
| 33-11 | 420076 | 90° Fitting For Air Line | 2 |  |
| 33-12 | 420143 | Buzze | 1 |  |
| 33-13 | 52K056 | Cup Head Bolt | 4 |  |
| 33-14 | 52K022A | Cabinet Door | 1 |  |
| 33-15 | 52K006A | Panel for Installing Element | 1 |  |
| 33-16 | 620082 | Terminal | 1 |  |
| 33-17 | 420087 | Fuse Base | 3 |  |
| 33-18 | 420086 | Fuse(FU) | 3 |  |
| 33-19 | 420085 | Fuse Cap | 3 |  |

| Item | Part# | Description | QTY. | Note |
| --- | --- | --- | --- | --- |
| 33-20 | 61K052 | Cup head bolt | 19 |  |
| 33-21 | 420135 | Timer Relay Base | 2 |  |
| 33-22 | 420141 | Intermediate Relay(KA) | 1 |  |
| 33-23 | 420083 | Timer Relay(KT) | 1 |  |
| 33-24 | 420084A | AC Contactor (KM) | 1 |  |
| 33-25 | 420140 | Thermal Relay(FR) | 1 |  |
| 33-26 | 420166 | 90° Fitting | 1 |  |
| 33-27 | 420077 | Air Solenoid Valve(Y2) | 1 |  |
| 33-28 | 201034 | Bleeding plug | 1 |  |
| 33-29 | 420134 | Transformer (TC) | 1 |  |
| Parts For SPX Electric Power Unit 220V/50HZ/1 Phase (See Fig.23) |
| 200-1 | 209082 | Motor | 1 |  |
| 200-2 | 209083 | Motor Connecting Shaft | 1 |  |
| 200-3 | 209084 | Valve Body | 1 |  |
| 200-4 | 209085 | Relief Valve | 1 |  |
| 200-5 | 209086 | Lock Washer | 4 |  |
| 200-6 | 209087 | Socket Bolt | 4 |  |
| 200-7 | 209088 | Inlet Pipe | 1 |  |
| 200-8 | 209089 | O-ring | 1 |  |
| 200-9 | 209090 | Filter | 1 |  |
| 200-10 | 209091 | Hex Bolt | 4 |  |
| 200-11 | 209092 | Reservoir | 1 |  |
| 200-12 | 209093 | Cup Head Bolt | 2 |  |
| 200-13 | 209094 | Cover for Capacitor | 1 |  |
| 200-14 | 209095 | Capacitor | 1 |  |
| 200-15 | 209096 | Rubber Gasket | 1 |  |
| 200-16 | 209097 | Hex Bolt | 1 |  |
| 200-17 | 209098 | Cover of Motor Terminal Box | 1 |  |
| 200-18 | 209110 | Oil Return Port | 1 |  |
| 200-19 | 209100 | Oil Outlet | 1 |  |
| 200-20 | 209162 | Hydraulic Solenoid Valve Nut | 1 |  |
| 200-21 | 209115 | Hydraulic Solenoid Valve Coil | 1 |  |
| 200-22 | 209116 | Hydraulic Solenoid Valve Body | 1 |  |
| 200-23 | 209117 | Release Valve Adjusting Rod | 1 |  |
| 200-24 | 420070 | Check Valve | 1 |  |
| 200-25 | 209106 | Gear Pump | 1 |  |
| 200-26 | 209107 | Oil Return Pipe | 1 |  |
| 200-27 | 209108 | Filter Cap | 1 |  |

| Parts For PEAK Electric Power Unit 220V/50HZ/1 Phase (See Fig.24) |
| --- |
| Item | Part# | Description | QTY. | Note |
| 200A-1 | 209082A | Motor | 1 |  |
| 200A-2 | 209083A | Motor Connecting Shaft | 1 |  |
| 200A-3 | 209084A | Valve Body | 1 |  |
| 200A-4 | 209085A | Relief Valve | 1 |  |
| 200A-5 | 209113 | Throttle Valve | 1 |  |
| 200A-6 | 209086A | Lock Washer | 4 |  |
| 200A-7 | 209087A | Socket Bolt | 4 |  |
| 200A-8 | 209088A | Inlet Pipe | 1 |  |
| 200A-9 | 209089A | O-ring | 1 |  |
| 200A-10 | 209090A | Filter | 1 |  |
| 200A-11 | 209091A | Hex Bolt | 4 |  |
| 200A-12 | 209092A | Reservoir | 1 |  |
| 200A-13 | 209093A | Screw | 4 |  |
| 200A-14 | 209094A | Cover for Capacitor | 2 |  |
| 200A-15 | 209095A | Start Capacitor | 1 |  |
| 200A-15A | 209095B | Running Capacitor | 1 |  |
| 200A-16 | 209096A | Rubber Gasket | 2 |  |
| 200A-17 | 209097A | Hex Bolt | 2 |  |
| 200A-18 | 209098A | Cover of Motor Terminal Box | 1 |  |
| 200A-19 | 209110A | Oil Return Port | 1 |  |
| 200A-20 | 209100A | Oil Outlet | 1 |  |
| 200A-21 | 420070A | Check Valve | 1 |  |
| 200A-22 | 209162A | Hydraulic Solenoid Valve Nut | 1 |  |
| 200A-23 | 209115A | Hydraulic Solenoid Valve Coil | 1 |  |
| 200A-24 | 209116A | Hydraulic Solenoid Valve Body | 1 |  |
| 200A-25 | 209117A | Release Valve Adjusting Rod | 1 |  |
| 200A-26 | 209106A | Gear Pump | 1 |  |
| 200A-27 | 209107A | Oil Return Pipe | 1 |  |
| 200A-28 | 209108A | Filter Cap | 1 |  |

| Parts For PEAK Electric Power Unit 380V/50HZ/3 Phase (See Fig.24) |
| --- |
| Item | Part# | Description | QTY. | Note |
| 200B-1 | 209118 | Motor | 1 |  |
| 200B-2 | 209083A | Motor Connecting Shaft | 1 |  |
| 200B-3 | 209084A | Valve Body | 1 |  |
| 200B-4 | 209085A | Relief Valve | 1 |  |
| 200B-5 | 209113 | Throttle Valve | 1 |  |
| 200B-6 | 209086A | Lock Washer | 4 |  |
| 200B-7 | 209087A | Socket Bolt | 4 |  |
| 200B-8 | 209088A | Inlet Pipe | 1 |  |
| 200B-9 | 209089A | O-ring | 1 |  |
| 200B-10 | 209090A | Filter | 1 |  |
| 200B-11 | 209091A | Hex Bolt | 4 |  |
| 200B-12 | 209092A | Reservoir | 1 |  |
| 200B-13 | 209097A | Hex Bolt | 2 |  |
| 200B-14 | 209098A | Cover of Motor Terminal Box | 1 |  |
| 200B-15 | 209110A | Oil Return Port | 1 |  |
| 200B-16 | 209100A | Oil Outlet | 1 |  |
| 200B-17 | 420070A | Check Valve | 1 |  |
| 200B-18 | 209162A | Hydraulic Solenoid Valve Nut | 1 |  |
| 200B-19 | 209115A | Hydraulic Solenoid Valve Coil | 1 |  |
| 200B-20 | 209116A | Hydraulic Solenoid Valve Body | 1 |  |
| 200B-21 | 209117A | Release Valve Adjusting Rod | 1 |  |
| 200B-22 | 209106A | Gear Pump | 1 |  |
| 200B-23 | 209107A | Oil Return Pipe | 1 |  |
| 200B-24 | 209108A | Filler Cap | 1 |  |

# Text boxes

Bolting

Fig. 3

Power source inlet 4*25mm²

Air source inlet

(50PVC tube

Fig. 2

Fig. 4

Fig. 5

PII

Platform

PI

Platform

Fig. 6

Fig. 7

PII

PI

Fig. 8

PII

PI

Fig. 9

Connecting the air source by the oil-water separator

Clockwise to increase the air pressure

Counter-clockwise        to reduce the air pressure

Adjust the air pressure to 0.4~0.6MPa

Fig. 10

This point shows the present rated current value

Using cross screwdriver to adjust rated current value of thermal relay

Earth Wire

Power Wire

Hydraulic solenoid valve

Low Limit switch

Motor Wire

Fig. 12

Fig. 11

Fig. 13

Earth Wire

Power Wire

Hydraulic solenoid valve

Low Limit switch

Motor Wire

Fig. 14

Fig. 15

Using the Level Bar for the measurement

PI

PII

33

Fix the control cabinet with anchor bolts

1000mm

Fix the lift with anchor bolts

Adjusting with Shim

Fig. 16

Fig. 17

49

Clearing

Drilling

50

Fig. 18

51

Drilling

Clearing

Bolting

Tighten

Fig. 19

Fig. 20

DOWN 1

380V/50HZ/3 phase

220V/50HZ/1 Phase

Fig. 24

Fig. 25

Check valve

Hydraulic solenoid valve

Capacitor

Relief valve

Auxiliary hole

Auxiliary hole

Oil return port

Oil Outlet

Fig. 27

Start capacitor

Running capacitor

Relief valve

Throttle valve

Hydraulic solenoid valve

Oil return port

Check valve

Oil Outlet

Fig. 26

Relief valve

Oil return port

Throttle valve

Hydraulic solenoid valve

Check valve

Oil outlet

Fig. 1

Tighten

Fig. 21

Fig. 22

Fig. 23

Oil Filling Position

Fig. 28

Normal Working Position

Fig. 29

DOWN 2

LOCK

UP

POWER SWITCH

56

Fig. 30

3 Phase

Single Phase

07/2013

72216102

46

48

45

22

33-20

33-15

47

Add grease to lubricate regularly

Add grease to lubricate regularly

90mm

High Limit switch

High Limit switch